## Slide 1: PERFORMANCE OF REVIEW AND ASSESSMENT OF SITING DOCUMENTS
    By
    AKE .O. ADERINOYE

## Slide 2: TABLE OF CONTENTS
Objective of Review & Assessment
Basic reference for development of SER
Review Phases
  Format and Contents
  Detailed Review
  Review Against Operating Experience Feedback

## Slide 3: REVIEW & ASSESSMENT
  Review and assessment is one of the major functions of a Regulatory Body
  A thorough review and assessment of Site Evaluation Report (SER) is performed by regulatory body:
    The effects of external events (natural origin or human induced)
    The characteristics of the site and its environment that could influence the transfer to persons and the environment of radioactive material that has been released;
    The population density and population distribution and other characteristics of the external zone that may affect the possibility of implementing emergency measures.
  Ensure the design basis and its adequacy for an NPP have been fully established and authorization for Site registration may be granted.

## Slide 4: OBJECTIVE OF REVIEW & ASSESSMENT
    The following are the objectives of review and assessment:
    To evaluate submissions with reference to regulatory requirements as defined by national regulations, regulatory guides, IAEA safety standards, industrial codes etc
    To determine whether the site complies with the safety objective, principles and criteria
    To ensure that the site is within safe envelop (making sure NO BLINDSPOT, nothing undefined as regards site of choice, we must have ALL INFORMATION)

## Slide 5: BASIC REFERENCE FOR R&A OF SER
Acceptance Criteria against which review is performed is agreed between the regulator and applicant before the submission of SER and is used by the review team.
The documents which serve as reference for acceptance criteria are:
  Regulatory Guide 1.70 “Standard Format and Content of Safety Analysis Reports for Nuclear Power Plants”
  National Regulations
  NRC regulatory Guides
  IAEA Safety Standards
  National & International Experience Feedback

## Slide 6: REVIEW PHASES
There are 3 PHASES OF REVIEW AND ASSESSMENT of the SER
During the Phase 1, what we do as a RB is to check the format and content for completeness by comparing the SER with the USNRC Regulatory Guide, RG 1.70 (2 – 3 weeks)
RG 1.70 has different chapters addressing different areas of the NPP
RG 1.70 chapter 2 addresses site characteristics and its divided into five (5) different sections. These sections give specific parameters required to determine suitability of a site.
Each section has its objective(s) and the specific parameters required to address such objectives.
Its after confirming completeness of the required parameters, that we will go the second phase of review and assessment (Phase 2) - Detailed review in the light of Regulations, Regulatory Guides and Standard Review Plans (SRP) (5 – 6 or 8 months)

## Slide 7: REGULATORY GUIDANCE
      NUREG-800 Standard Review Plan
      10 CFR part 100, "Reactor site Criteria“
      RG 4.7, General Site Suitability Criteria for Nuclear Power Stations
      RG 1.23, Meteorological Monitoring Programs for Nuclear Power Plants
      RG 1.91, Evaluations of Explosions Postulated To Occur on Transportation Routes near Nuclear Power Plants
      RG 1.111, Methods for Estimating Atmospheric Transport and Dispersion of Gaseous Effluents in Routine Releases from Light-Water-Cooled Reactors
      RG 1.132, Site Investigations for Foundations of Nuclear Power Plants
      RG 1.138, Laboratory Investigations of Soils and Rocks for Engineering Analysis and Design of Nuclear Power Plants
      RG 1.145, Atmospheric Dispersion Models for Potential Accident Consequence Assessments at Nuclear Power Plants 1 02/1983
      RG 1.60, Design Response Spectra for Seismic Design of Nuclear Power Plants

## Slide 8: REGULATORY GUIDANCE
      NS-R-3, "Site Evaluation for Nuclear Installations"
      NS-G-3.1, "External Human Induced Events in Site Evaluation for Nuclear Power Plants
      NS-G-3.2, "Dispersion of Radioactive Material in Air and Water and consideration of
      Population Distribution in Site Evaluation for Nuclear Power Plants
      NS-G-3.3, "Evaluation of Seismic Hazards for Nuclear Power Plants
      NS-G-3.4, "Meteorological Events in Site Evaluation for Nuclear Power Plants
      NS-G-3.5, "Flood Hazard for Nuclear Power Plants on Coastal and River sites
      NS-G-3.6, "Geotechnical Aspects of Site Evaluation and Foundations for Nuclear Power Plants
      GSR Part 2 & 50-C-SG-Q9, "Quality Assurance in Siting"

## Slide 9: REVIEW PHASES cont…
The Third Phase (Phase 3) of review has to do with International Experience Feedback in NPP Siting (lessons learnt) based on:
International reports
Incident reporting
Literatures from nuclear industry with close relations to the site
Engineering judgment
IRRS (Integrated Regulatory Review Service) reports applicable to the type of NPP proposed to be constructed: these reports can be downloaded from the IAEA website

## Slide 10: SCOPE OF SITE EVALUATION REPORT
1. Geography and Demography Site Location and Description Specification of Location Site Area Map Boundaries for Establishing Effluent Release Limits Exclusion Area Authority and Control Authority Arrangements for Traffic Control Abandonment or Relocation of Roads Population Distribution Population within 10 & 80 km Radius (latest Census & projected) Transient Population Low Population Zone Population Centers Population Density | Nearby Industrial, Transportation and Military Facilities Locations and Routes Description of Facilities, Products and Materials Pipelines Waterways Airports Projections of Industrial Growth Military Facilities Railways Roads Mining and Quarrying Evaluation of Potential Accidents Determination of Design Basis Events Effects of Design Basis Events Offsite Power
10

## Slide 11: SCOPE OF SITE EVALUATION REPORT
3. Meteorology Regional Climatology General Climate Regional Meteorological Conditions for Design and Operating Bases Local Meteorology Normal and Extreme Values of Meteorological Parameters Local Meteorological Conditions for Design and Operating Bases Onsite Meteorological Measurements Program. Emergency preparedness plan Short Term Diffusion Estimates Long Term Diffusion Estimates | Hydrologic Engineering Hydrologic Description Floods Probable Maximum Flood (PMF) on Streams and Rivers Water Level Determination Potential Dam Failure, Seismically Induced Probable Maximum Tsunami Flooding Cooling Water Canals and Reservoirs Flooding Protection Requirements Low Water Considerations Dispersion, Dilution and Travel Times of Accidental Releases of Liquid Effluents in Surface Waters Ground Water
11

## Slide 12: SCOPE OF SITE EVALUATION REPORT
5. Geology, Seismology and Geotechnical Engineering Basic Geologic and Seismic Information Regional Geology Vibratory Ground Motion Surface Faulting Stability of Subsurface Materials and Foundations Response of Soil and Rock to Dynamic Loading Liquefaction Potential Techniques to improve sub-surface Conditions Subsurface instrumentation Stability of Slopes
12

## Slide 13: ASSESSMENT /AUDIT CALCULATIONS
Seismic Hazard Analysis
Site Response Analysis
Tsunami hazard Analysis
Flooding Hazard Analysis
Radiological Dose Assessment
13

## Slide 14: THANK YOU